## Slide 1
DEFENSE RESEARCH & DEVELOPMENT ORGANISATION (DRDO)
Smart Scan Strategy for Electronic Warfare (ES) Receivers
Slew-Regularized Restless Multi-Armed Bandit (RMAB) Scheduling with Sub-Microsecond RTOS Compliance
Problem Statement ID: 26055 | Team Smart Scan | Aggregate Intercept Gain: 79.03% P_int

## Slide 2
DRDO EW SMART SCAN | PROBLEM STATEMENT 26055
The Tactical Problem Statement (DRDO 26055)
Passive ES & RWR Mission
• Passive radar warning receivers (RWR) must detect, intercept, and classify hostile emissions.
• Operate entirely silently to protect own platform stealth.
• Must build a real-time Electronic Order of Battle (EOB) under dense signal clutter.
The Bandwidth Dilemma
• Threat spectrum spans 0.5 GHz to 18 GHz (UHF Early Warning to Ku-band Fire Control).
• Instantaneous Receiver Bandwidth (B_inst) is strictly limited to 500 MHz - 1 GHz.
• The spectrum must be partitioned into K = 16 discrete sub-bands.
• Listening to Band 1 leaves Bands 2-16 entirely deaf.
The Tactical Stakes
• Modern AESA & LPI radars emit brief microsecond bursts with 1%-5% duty cycles.
• Missing high-priority fire-control illuminations leads to undetected missile locks.
• Requires intelligent scheduling to outpace agile adversaries.

## Slide 3
DRDO EW SMART SCAN | PROBLEM STATEMENT 26055
Failure Analysis of Legacy Scanning Paradigms
1. Deterministic Round-Robin Sweep
• Sequential stepping (0 -> 1 -> ... -> K-1) designed for 1970s analog CW radars.
• Against 1%-5% duty cycle AESA radars, capture probability is bounded by duty cycle (~4.3%).
• Over 95.6% of hostile pulses slip entirely through inter-sweep blind periods.
2. Uniform Random Search
• Memoryless stochastic jumping prevents predictability but ignores historical data.
• Maximizes synthesizer Phase-Locked Loop (PLL) settling dead-time.
• Wastes up to 42% of mission time in blanking transitions.
3. Pure Greedy (Max-Belief Camping Trap)
• Always selects the channel with the highest instantaneous pulse count.
• Camps on a single loud emitter, starving the remaining 15 sub-bands for up to 5,870 ms.
• Drops overall emitter situational awareness down to 33.3%.
4. ε-Greedy / Unconstrained Exploration
• Random exploration steps cause wideband frequency jumps (e.g., Band 0 to 15).
• Incurs maximum 45 µs PLL lock penalty, resulting in severe blanking dead-time.
• Fails to balance exploration utility against hardware tuning costs.

## Slide 4
DRDO EW SMART SCAN | PROBLEM STATEMENT 26055
Modeling Real-World RF Hardware Physics
Synthesizer Slew
• Voltage-Controlled Oscillators (VCOs) and YIG synthesizers require charge-pump settling time.
• Retuning is not instantaneous; physical voltage shifts take finite microseconds.
• Ignoring slew physics causes simulated algorithms to fail in physical deployment.
Logarithmic Penalty
• Settling time scales logarithmically with hop distance:
• t_settle = 5.0 + 12.0 · log2(1 + |Δk|) µs
• Adjacent tuning takes ~5 µs; full 16-band hops take up to 45 µs.
• Front-end must be blanked during settling to prevent false alarms.
Noise & Pd Modeling
• Thermal noise floor (kTBF) dictates receiver sensitivity.
• Swerling target fluctuation models simulate cross-section fades.
• Binomial masking injects Pd < 1.0 (15%-30% pulse loss) to ensure robust filtering.

## Slide 5
DRDO EW SMART SCAN | PROBLEM STATEMENT 26055
Mathematical Core: Bayesian Restless Bandits (RMAB)
Why RMAB over Deep RL?
• Non-Stationary Adversaries: Offline neural networks suffer catastrophic distribution shifts against unfamiliar hopping or jittered PRIs.
• Deterministic Guarantees: DRDO mandates hard worst-case latency bounds (≤ 60 ms starvation), which black-box deep learning cannot guarantee.
• Microsecond Inference: Analytical Bayesian updates execute in microseconds, ideal for embedded hardware.
Conjugate Beta-Bernoulli Updates
• Zero-Prior Initialization: Maintains expected belief E[θ] = α / (α + β) for each sub-band.
• Hit Rule (h > 0): α_k ← α_k + min(h, 10.0), rapidly driving belief toward 1.0.
• Step-on-Miss (h = 0): β_k ← β_k + 2.0, instantly suppressing belief to vacate empty channels.
• Markovian Aging: Unvisited bands decay smoothly (α, β × 0.995) to model uncertainty over time.

## Slide 6
DRDO EW SMART SCAN | PROBLEM STATEMENT 26055
The Slew-Regularized Whittle Index Formula
I_k(t) = [E[θ_k] + T_hop(k)] · Φ_k(t) · [1 + 0.8·ln(1+C_k)] + λ · ((t - τ_k) / τ_max) - κ · log2(1 + |Δk|)
Fuses Bayesian belief, cross-band frequency hop prediction, temporal burst periodicity, track density, strict anti-starvation bounds, and physical synthesizer blanking penalties into a single microsecond decision metric.
E[θ_k] + T_hop(k)
Bayesian Belief & Hopping
Tracks active emitter probability and leverages online Markov transition matrices to pre-tune ahead of agile frequency hoppers.
Φ_k(t) Kernel
Temporal Recurrence
Gaussian probability spike modeling pulse repetition phase to predict exact arrival timing of periodic radar bursts.
λ · (t - τ_k) / τ_max
Anti-Starvation Bound
Linear urgency inflation. As starvation nears τ_max = 60 ms, index approaches +∞, enforcing DRDO compliance.
- κ · log2(1 + |Δk|)
Synthesizer Penalty
Subtracts utility for distant frequency jumps, restricting wide slews unless justified by high-threat reward.

## Slide 7
DRDO EW SMART SCAN | PROBLEM STATEMENT 26055
Real-Time Signal Processing & O(1) Memory Architecture
O(1) Static Circular Ring Buffers
• OS Heap Limitation: Standard dynamic lists (malloc/vector) cause heap fragmentation and Garbage Collection latency spikes (10-50 ms pauses) on RTOS.
• Static Pre-Allocation: Allocates fixed memory buffers (N = 2048) exactly once at system boot.
• Modulo Pointer Arithmetic: idx = (head + i) % capacity guarantees strict O(1) insertion time.
• Graceful Degradation: Automatically drops oldest pulses during extreme jamming bursts to preserve microkernel stability.
SDIF De-interleaving & Threat Classification
• Multi-Order Time Differences: Computes Δti(d) = ToA(i+d) - ToA(i) with exponential discounting (0.85^(d-1)) to extract true PRIs.
• Harmonic Cancellation: Mathematically tests candidate peaks and discards integer-ratio sub-harmonics (2x, 3x) within ±5% tolerance.
• MIL-STD Threat Mapping:
• - PRF > 4000 Hz: Fire Control / Missile Guidance (CRITICAL)
• - 1000-4000 Hz: Acquisition & Tracking (HIGH)
• - PRF < 1000 Hz: Surveillance / Early Warning (MEDIUM)

## Slide 8
DRDO EW SMART SCAN | PROBLEM STATEMENT 26055
Empirical Validation: 3,693,275 Pulses Across 23 Splits
Scheduling Strategy | Macro Mean P_int | Median P_int | Aggregate Weighted P_int | Win Rate vs RMAB
Round-Robin (Legacy 1970s) | 4.30% | 4.37% | 4.38% | 0 / 23 (0.0%)
Uniform Random Search | 3.55% | 3.52% | 3.61% | 0 / 23 (0.0%)
Pure Greedy (Max-Belief) | 37.76% | 20.38% | 47.68% | 9 / 23 (39.1%)
ε-Greedy (ε = 0.15) | 43.59% | 42.79% | 60.41% | 3 / 23 (13.0%)
Adaptive Bayesian RMAB (Ours) | 59.10% | 64.00% | 79.03% | — (Baseline)

## Slide 9
DRDO EW SMART SCAN | PROBLEM STATEMENT 26055
Operational Guarantees: Starvation & Emitter Coverage
Strict Starvation Bound
• Target Revisit Ceiling: Strictly bounded at τ_max = 60.0 ms across all operational scenarios.
• Observed Peak: Maximum channel starvation across all 3.69M pulses peaked at 58.6 ms (mean 19.9 ms).
• Zero Violations: Exactly 0 out of 23 test splits exceeded the mandatory DRDO starvation limit.
Exposing the Greedy Fallacy
• Pure Greedy appears to score high raw pulse P_int on volume-heavy splits by camping on a single loud emitter.
• Catastrophic Collapse: In 7 major splits, Pure Greedy collapsed below 8% (dropping to 0.24% in test_11).
• RMAB Stability: Delivers robust 56%-85% P_int across all splits without ever failing.
Situational Awareness
• Emitter Coverage: Maintained a macro mean emitter discovery rate of 75.65% across all 989 test emitters.
• No Blind Spots: Prevents channel abandonment, ensuring secondary threat tracks are audited continuously.
• Balanced Tradeoff: Maximizes pulse capture while maintaining complete air picture.

## Slide 10
DRDO EW SMART SCAN | PROBLEM STATEMENT 26055
Embedded RTOS Feasibility & Hardware Profiling
Measured Python Benchmark (10,000 Dwells)
• Action Selection (select_action): 19.2 µs mean (24.1 µs at 99th percentile).
• Posterior Update (update_beliefs): 6.4 µs mean (8.2 µs at 99th percentile).
• Total Decision Cycle: ~25.6 µs total execution time.
• Timing Headroom: Leaves a robust 42.2% safety margin within a standard 45 µs hardware dwell budget.
Embedded Hardware Translation
• POSIX Resource Manager: Translating core math to compiled C in a microkernel architecture (e.g., QNX Neutrino) reduces cycle time to < 1.2 µs.
• FPGA Synthesis: Fixed-point RTL implementation on a Xilinx Zynq UltraScale+ RFSoC executes parallel index evaluation in < 180 ns.
• Hard Real-Time: Zero dynamic memory allocations guarantee deterministic execution deadlines for military avionics.

## Slide 11
DRDO EW SMART SCAN | PROBLEM STATEMENT 26055
Tactical Cockpit & C2 Interoperability Architecture
Streamlit Command Center
• Unified Dashboard: Complete operational control without command-line overhead.
• Interactive Visualizations: Real-time electromagnetic waterfall display overlaying LO scan trajectories.
• Polar RWR Scope: 360° Plan Position Indicator color-coding threat lethality.
System Healthcheck Suite
• Pre-Flight Verification: Automated unit testing verifying HDF5 integrity and belief convergence.
• Circular Buffer Audits: Confirms O(1) ring buffer stability and SDIF extraction.
• Regression Control: Guarantees zero runtime faults before deployment.
STANAG 4607 & EOB Export
• NATO Standardization: Instantaneous export of de-interleaved tracks into STANAG 4607 JSON.
• Tactical CSV Reports: Complete Electronic Order of Battle (EOB) tables for operator review.
• EA Handoff: Seamless target handoff to Electronic Attack (EA) countermeasures.

## Slide 12
DRDO EW SMART SCAN | PROBLEM STATEMENT 26055
Conclusion: DRDO Problem Statement 26055 Solved
Core Accomplishments
• 79.03% Aggregate Intercept Probability across 3.69M Turing pulses (18x baseline gain over Round-Robin).
• Strict Starvation Compliance: 100% adherence to the mandatory ≤ 60 ms revisit limit (observed peak 58.6 ms).
• RTOS-Ready Firmware: Zero heap allocations with O(1) static circular buffers and graceful buffer degradation.
Deliverable Assets
• Fully Tested Codebase: Modular architecture with config.yaml parametrization and strict type-hinting.
• Tactical Command Cockpit: Streamlit UI with multi-split benchmarking and live RWR scopes.
• Comprehensive Documentation: 50+ page technical thesis and master viva voce compendium ready for jury defense.